| PHYSICAL SPECIFICATION |
| --- |
| Nominal Voltage Nominal Capacity (10HR) | 12V 40Ah |  |
| Dimension | Length Width Container Height Total Height | 198±1mm （7.80 inches) 166±1mm (6.54 inches) 170±1mm (6.77 inches) 170±1mm (6.77 inches) |  |
| Weight | Approx. 14.2 Kg ( 31.3lbs) |  |
| Standard Terminal | Bolt-and-nuts lead terminal Bolt Type: M5 |  |
| ELECTRICAL SPECIFICATION |
| Characteristics | Discharge curves @ 25℃ (77 °F) |
| Capacity | 10 hour rate (4A) 5 hour rate (6.8A) 3 hour rate (10A) 1hour rate (24A) | 40Ah 34Ah 30Ah 24Ah |  |
| Capacity affected by temperature | 40℃ （104 0F） 25℃ （77 0F） 0℃ （32 0F） | 102% 100% 85% |  |
| Internal Resistance | Full charged battery (25℃,77 0F) 7mΩ |  |
| Constant Voltage Charge | Cycle | Initial Charging Current less than 10A Voltage 14.1~14.4V at 25℃ (77 0F ) Temperature Coefficient –18mV/℃ |  |
|  | Standby | No limit on Initial Charging Current Voltage 13.5~13.8V at 25℃ (77 0F ) Temperature Coefficient –18mV/℃ |  |